## SNIFFI HANDHELD - PARTS LIST
### Computing & Display
- Raspberry Pi 4 - 8GB RAM (future-proof for multi-shift data storage)
- MicroSD Card - 64GB or 128GB (for OS and local data storage)
- 4" Touchscreen - Capacitive touch, HDMI connection, USB-powered
  - Resolution: TBD (likely 800x480 or 1024x600)
### Power System
- 30,000 mAh USB Battery Pack - Multiple USB outputs, 5V
- USB Hub - Powered, at least 4 ports (for GPS, touchscreen power, sensor array, potential expansion)
### Sensor Array (16 sensors total)
- Custom PCB with Arduino Mega - USB Type-B connection to Pi
- SM4 NO2 20 Module
- DHT22 Digital Temperature and Humidity Sensor Module
- MQ-131 High
- MQ-131 Low
- MQ-137 Sensor Module
- ZE08-CH2O Electrochemical Formaldehyde Sensor Module
- MQ-2 Sensor Module
- CJMCU-811 Sensor Co2
- ZP07 Air Quality Detection Module
- MQ-136 Sensor Module
- ZE03-SO2 Module
- MQ-135 Air Quality Sensor Module
- MQ-4 Methane Gas Sensor
- MQ-6 Gas and Smoke Sensor Module
- MQ-7 Smoke Detection Module
- MQ-8 Methane Gas Sensor Module
### Airflow System
- Two 40mm Fans - 5V DC (controlled via MOSFET switch from Pi GPIO)
- MOSFET Switch Module - Same as Patrol (for fan control)
- Intake Mesh Screen - Fine mesh to prevent debris, covers sensor array at narrow end
- Dimensions: 120mm x 240mm sensor array coverage
### Navigation & Audio
- USB GPS Module - Same as Patrol unit
  - Dimensions: 1.5" x 1.5" x 0.75"
  - USB connection with cord for positioning flexibility
- 3W Speaker - 5V powered, diameter TBD (20-28mm typical)
### Cables & Connections
- USB Type-B to USB Type-A Cable - For Arduino Mega to Pi connection
- HDMI Cable - Short/right-angle for touchscreen connection
- USB Power Cables - Various lengths for internal component connections
- GPIO Jumper Wires - For MOSFET control connections
### Mechanical/Housing
- Custom Enclosure - Egg-shaped, smooth rounded edges
  - Dimensions: ~120mm x 240mm footprint x 2-3" thick (tapered)
  - Narrow end: ~2" thick (intake/sensor end)
  - Wide end: ~3" thick (exhaust/handle attachment)
- Webbing Slots/Loops - For K9 vest mounting (hardware TBD)
- Detachable Handle - Clip-on mechanism (design TBD)
- Power Button - Illuminated on/off switch
### Estimated Dimensions
- Overall: 240mm (9.4") long x 120mm (4.7") wide
- Thickness: Tapered from 2" (narrow/intake end) to 3" (wide/exhaust end)
- Weight: TBD (depends on battery pack and enclosure material)
### USB Port Usage Count
1. GPS Module
2. Touchscreen (power)
3. Sensor Array (Arduino Mega)
4. One spare for future expansion